## Slide 1: Unit -III
The 8255 Programmable Peripheral Interface

## Slide 2: Syllabus
8255 PPI various modes of operation and interfacing to 8086.
Interfacing keyboard
Display
Stepper motor interfacing
D/A and A/D converter.

## Slide 3: 8255 Block diagram

## Slide 5: 8255 programming & operation
Bit D7 of the control register specifies either I/O function or the Bit Set/Reset function. 8255 has three operation modes: mode 0, mode 1, and mode2.

## Slide 8: 8255 programming & operation
Mode 0: ( I/O mode)
  Ports A, B, and C can be individually programmed as input or output ports.
  Port C is divided into two 4-bit ports which are independent from each other.
Mode 1:( Strobed I/O)
Ports A and B are programmed as input or output ports.
  Port C is used for handshaking.
Port A -Input:
PC3 PC4 PC5 – control
PC6 PC7 – I/O
Port A -output:
PC3 PC6 PC7 – control
PC4 PC5– I/O
Port B input /output:
PC0 PC1 PC2– control mode1/mode2

## Slide 9: 8255 programming & operation
Mode2:(Strobed Bidirectional bus I/O)
  Port A is programmed to be bi-directional.
  Port C is for handshaking.
  Port B can be either input or output in mode 0 or mode 1.
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
1 | 1 | X | X | X | 1/0 | 1/0 | 1/0
I/O mode
Mode2 for PortA PortB I/O PC0-PC2 I/O
mode for portB

## Slide 10: ADC interfacing

## Slide 11: ADC interfacing

## Slide 13: ADC interfacing
Algorithm:
Configure the ports.
Select the analog input.
Give start of conversion pulse to the ADC.
Wait till the EOC goes high.
If EOC=1, read digital data.

## Slide 14
MOV AL, 98h ;initialise 8255 as
OUT CWR, AL
MOV AL, 02h ;Select I/P2 as analog
OUT Port B, AL ;input.
MOV AL, 01h ;Give start of conversion
OUT Port C, AL ; pulse to the ADC
MOV AL, 00h
OUT Port C, AL
WAIT: IN AL, Port C ;Check for EOC by
RCL AL,01H ; reading port C upper and
JNC WAIT
IN AL, Port A ;If EOC, read digital equivalent
HLT ;Stop.

## Slide 15: Instruction timing and delay loops
 |  | Clock cycles
 | MOV CX, N | 4 = C0
delay : | NOP | 3
 | NOP | 3 = CL
 | LOOP delay | 17 or 5

## Slide 16: Instruction timing and delay loops
C0 : No. of cycles for the instructions that execute only once.
CL : total no. of cycles for the instructions inside the loop.
CT: no. of clock cycles to produce the desired delay.
ex: for 1ms delay CT = 1ms = 5000
(assuming 5Mhz freq.) 1/5Mhz

## Slide 17: Instruction timing and delay loops
CT = C0 + N(CL)-12
N = (CT - C0 + 12)/CL
N = (5000 – 4 + 12)/(3+3+17)
= 0DAH

## Slide 18: Instruction timing and delay loops
Calculate the value of N for the following sequence with a delay value of 50ms.(assuming operating freq of 10Mhz)
 |  | Clock cycles
 | MOV CX, N | 4
delay : | DEC CX | 2
 | JNZ delay | 16 or 4

## Slide 19: DAC interfacing

## Slide 20: DAC interfacing
Interfacing DAC 0800 with an 8086 CPU
running at 8MHZ and write an assembly language program to generate a saw tooth waveform of period 1ms with Vmax 5V.

## Slide 21
MOV AL,80h ;make all ports output
OUT CWR, AL
again: MOV AL,00h ;start voltage for ramp
back : OUT PA, AL
CALL delay
INC AL
CMP AL, 0FFh
JB back
JMP again
Delay PROC NEAR
MOV CX,03H ;delay for 1 ms
LOOP $
Delay ENDP

## Slide 22: Keyboard interfacing
Types of switches:
  Mechanical switches
  Membrane switches
  Capacitive switches
  Hall effect switches

## Slide 23: Keyboard interfacing
Three major tasks:
  Detect a key press.
  Debounce the key press.
  Encode the key press.

## Slide 24: Key debounce

## Slide 27
Stepper motor interfacing

## Slide 28: Stepper motor interfacing

## Slide 29
Stepper motor interfacing
Motion | Step | A | B | C | D
Clock wise | 1 | 1 | 0 | 0 | 0
 | 2 | 0 | 1 | 0 | 0
 | 3 | 0 | 0 | 1 | 0
 | 4 | 0 | 0 | 0 | 1
 | 5 | 1 | 0 | 0 | 0
Anti clockwise | 1 | 1 | 0 | 0 | 0
 | 2 | 0 | 0 | 0 | 1
 | 3 | 0 | 0 | 1 | 0
 | 4 | 0 | 1 | 0 | 0
 | 5 | 1 | 0 | 0 | 0

## Slide 30: Stepper motor interfacing
Design a stepper motor and write an ALP to rotate shaft of 4-phase stepper motor.
  In clock wise 5 rotations
  In anti clock wise 5 rotations
  The port A address is 0740h. The stepper motor has 200 rotor teeth. PA0 drives winding Wa(winding a), winding Wb, and so on. It has an internal delay of 10ms.

## Slide 31: Stepper motor interfacing